## Slide 1
ELECTRICITY & MAGNETISM
A journey from invisible fields to moving machines
CLASS 8 • DISCOVER • TEST • EXPLAIN
Big question: How can an electric current make something magnetic—and make it move?
Teacher-led lesson • Interactive demonstrations • Quick challenges
Notes: Open with curiosity. Ask students to predict what the compass will do before explaining.

## Slide 2
Start with a mystery
Observe first. Explain after.
02
A compass needle turns near a wire carrying current.
No magnet is touching the compass. So what is acting on it?
COMPASS
CURRENT ON
Predict → Observe → Explain
Notes: Let students observe and propose explanations. Avoid giving away the answer immediately.

## Slide 3
Today’s mission
By the end, students should be able to…
03
01
Describe magnetic domains
Use a simple model to explain magnetisation.
02
Explain compass direction
Connect Earth’s magnetic field with a freely suspended magnet.
03
Link electricity and magnetism
Explain why current creates a magnetic field.
04
Explain motion and induction
Describe the motor effect and how changing magnetic conditions can induce current.
Notes: Read learning goals aloud and return to them at the end.

## Slide 4
Mission 1 • The circuit
A magnetic effect begins with moving electric charge.
04
A complete path lets current flow. An open switch breaks the path.
Cell supplies electrical energy
Closed switch → complete path → current flows
Open switch → broken path → no sustained current
The bulb glows only when the circuit is complete
CELL
SWITCH
BULB
CHECK: What changes when the switch opens?
Notes: Emphasise complete circuit and current flow. The diagram is schematic, not a wiring instruction.

## Slide 5
Mission 2 • Inside a magnet
A useful model: magnetic domains.
05
In many magnetic materials, tiny atomic magnetic moments group into regions called domains.
Unmagnetised piece
Magnetised piece
Directions mostly cancel
Many domains point the same way
Important: domains are regions containing many atomic magnetic moments—not individual molecules.
Notes: Domain model is simplified. Domains contain many atomic magnetic moments, not individual molecules.

## Slide 6
Mission 3 • Magnetic rules
Poles tell the story.
06
LIKE POLES
N
N
← →
Repel: N–N or S–S
UNLIKE POLES
N
S
→ ←
Attract: N–S
Animation idea: move the magnets together and watch their motion change—arrows alone are not the whole story.
Notes: Students should learn the rule and connect it to observable motion. Real magnets have field patterns, not visible force arrows.

## Slide 7
Mission 4 • Earth is a giant magnet
Why does a freely suspended compass point approximately north–south?
07
A compass needle aligns with the local magnetic field. Earth has a magnetic field, so the needle settles along its direction.
The compass does not point to geographic north with perfect accuracy everywhere: magnetic and geographic north differ.
N
EARTH'S MAGNETIC FIELD
Notes: Explain magnetic north vs geographic north in age-appropriate language; a compass aligns with the local magnetic field.

## Slide 8
Mission 5 • Electricity makes magnetism
Hans Christian Ørsted • 1820
08
During a demonstration, Ørsted observed that a nearby compass needle deflected when current flowed in a wire.
Conclusion: an electric current produces a magnetic field around the conductor.
Reverse the current → the field direction reverses.
I
Magnetic field lines circle the wire
Notes: Historical story is based on the 1820 observation of compass deflection by current.

## Slide 9
Mission 6 • Build an electromagnet
A coil carrying current can magnetise an iron core.
09
More coil turns usually make the field stronger (same current and geometry).
More current generally strengthens the field.
Switch off the current → the electromagnet’s field greatly reduces.
Reverse current → the poles swap.
CELL
IRON CORE
Paper clips are attracted when the coil is energised.
Notes: Strength trends are qualitative; exact field depends on core, geometry, current and other factors.

## Slide 10
Mission 7 • The motor effect
A current-carrying conductor in a magnetic field can experience a force.
10
In a simple motor, forces act on opposite sides of a current-carrying coil. The forces can turn the coil.
Reverse current OR reverse the magnetic field → the force direction reverses.
A commutator in a simple DC motor reverses coil current every half-turn to keep rotation going in the same overall direction.
N
S
COIL
Notes: Use the diagram to identify the field, current and force. Keep motor operation as a simplified classroom model.

## Slide 11
Mission 8 • Make electricity from motion
Faraday’s discovery • 1831
11
When the magnetic field through a coil changes, a voltage can be induced. If the circuit is closed, current can flow.
Move the magnet faster → usually a larger induced voltage.
Hold the magnet still relative to the coil → no changing flux, so no sustained induced voltage.
N
S
COIL
Mechanical energy → electrical energy
Notes: Emphasise changing magnetic flux. A stationary magnet and coil do not produce a sustained induced voltage in this simplified setup.

## Slide 12
Motor or generator?
Same electromagnetic relationship—different energy conversion.
12
MOTOR
Electrical energy
Mechanical motion
Current + magnetic field → force and motion
GENERATOR
Mechanical motion
Electrical energy
Changing magnetic flux → induced voltage
Both depend on electromagnetism, but the energy flow is opposite.
Notes: Compare energy conversion direction.

## Slide 13
A short history of invisible forces
Science grows through observations, experiments and better explanations.
13
c. 1600
William Gilbert
Studied magnetism; argued Earth behaves like a magnet.
1820
H. C. Ørsted
Observed compass deflection near a current-carrying wire.
1825
William Sturgeon
Built an early practical electromagnet.
1831
Michael Faraday
Demonstrated electromagnetic induction.
19th century
Motor development
Scientists and engineers developed practical electric motors.
Story thread: Earth’s magnetism → current makes a field → fields can move coils → changing fields can generate electricity.
Notes: Timeline is a short selection of historical milestones, not a complete history.

## Slide 14
Challenge round • Think before you answer
Use a partner discussion or quick show of hands.
14
1
What happens to the compass near a current-carrying wire?
Reveal/explain: It deflects because current produces a magnetic field.
2
What changes when the current direction is reversed?
Reveal/explain: The direction of the magnetic field reverses.
3
Why does a freely suspended compass settle roughly north–south?
Reveal/explain: It aligns with Earth’s local magnetic field.
4
What is the key difference between a motor and generator?
Reveal/explain: Motor: electrical → mechanical. Generator: mechanical → electrical.
Notes: Give students time to justify answers; ask follow-up questions rather than accepting memorised phrases.

## Slide 15
Exit ticket • Explain it in your own words
Three short responses before you leave.
15
A
Explain magnetic domains using the words “aligned” and “random.”
B
Describe one observation that shows electricity can create magnetism.
C
Explain one difference between a motor and a generator.
SAFETY: Use only approved low-voltage classroom equipment. Never connect experiments to mains electricity.
Next: open the companion interactive adventure to explore each system.
Notes: Collect the exit ticket to identify what needs reteaching. Safety is non-negotiable.